Drop Project

Scope: Allow a demonstrator to drop various objects, either individually or in pairs, in order to observe the behavior of the objects in free fall. Up to two objects will be selected with separate push buttons or switches. Once selected, the objects will be dropped with a single, separate push button providing for a nearly simultaneous release.

Concept: The objects will be suspended onto separate solenoid plungers. Two Arduino units communicating through a wireless connection, will be used to release the object(s). The current intention is to provide for up to a total of 10 solenoids. The previously selected solenoids will be activated upon pressing a single button.

An Arduino master routine will read the separate push button/switch selection(s) and encode them accordingly. Upon sensing that the activation button has been pressed, the routine will pass the solenoid(s) selected to the Slave routine via the wireless connection.

Upon receiving the data from the master routine, the slave routine will decode the bytes to determine the specific solenoid(s) to be activated. Once decoded, the Slave routine will energize the selected solenoid(s) to allow release of the previously loaded objects. After a 1 or 2 second delay, the routine will remove power from the solenoids, allowing them to reset for the next drop.